## Slide 1: Autonomous Navigation of E-Rickshaw using camera
Presented by:
Shreyas Tripathi (Electronics Engg.)
Tushar Khandelwal(Electronics Engg.)

## Slide 2: Contents
Motivation and Objectives
Overview
Approach/Methods
Social Impact
Progress Made
References

## Slide 3: Motivation
Motivation:
1. reduce road accidents : approx. 5 lakh accidents every year (officialy)
2. free up large amount of parking spaces
3. reduce the problem of traffic
4. decrease carbon emissions
5. conserve fuel

## Slide 4: Objectives
Provide autonomous and global navigation for autonomously navigating e-rickshaw
local path planning to avoid obstacles on the road and manoeuvre the vehicle properly on crowded roads
The data from the cameras is used for local path planning which is fed to a convolutional neural network (CNN) to map raw pixels to steering commands.

## Slide 5: Overview

## Slide 6: Local Navigation
Three cameras are mounted behind the windshield of the data-acquisition e-rickshaw. Time-stamped video from the cameras is captured simultaneously with the steering angle applied by the human driver
train a convolutional neural network (CNN) to map raw pixels from a single front-facing camera directly to steering commands
This steering command is obtained by tapping into the vehicle’s Controller Area Network (CAN) bus.
In order to make our system independent of the car geometry, we represent the steering command as 1/r where r is the turning radius in meters.
We will use an NVIDIA DevBox and Torch 7 for training and an NVIDIA DRIVETM PX self-driving car computer also running Torch 7 for determining where to drive

## Slide 7: Training Data Set
Training data contains single images sampled from the video, paired with the corresponding steering command (1/r).
We sample that video at 10 FPS. A higher sampling rate would result in including images that are highly similar.
Training data includes a higher proportion of frames that represent road curves.
We augment the data by adding artiﬁcial shifts and rotations to teach the network how to recover from a poor position or orientation.

## Slide 8: Architecture
9 layers, including a normalization layer, 5 convolutional layers and 3 fully connected layers
ﬁrst layer of the network performs image normalization
The convolutional layers were designed to perform feature extraction
The ﬁve convolutional layers with three fully connected layers leading to an output control value which is the inverse turning radius
. The fully connected layers are designed to function as a controller for steering.

## Slide 9: Social Impact
Stakeholders- Automobile industry, driver community, academia, public.
Institutional Arrangements- Fully- equipped labs, servers for processing big-data, high-quality cameras and sensors.
Social risks- Acceptance by the Government, acceptance by the public and the industry

## Slide 10: Till Now:
Dataset was recorded while vehicle was driven by human.
A small-scale prototype for driving model was prepared using microprocessor “Raspberry pi” with RTos implemented
Driving model using single camera is prepared by mimicking human decision-making approach for efficient and autonomous driving.
Basic algorithm has been implemented for PoC.

## Slide 11: References
Mariusz Bojarski , Davide Del Testa , Daniel Dworakowski , End to End learning for Self-Driving cars , Nvidia
Sebastian Thrun. “Path Planning for Autonomous Vehicles in Unknown Semi-structured Environments”.
Kaijun Zhou. “Local Path Planning of Driverless Car Navigation Based on Jump Point Search Method Under Urban Environment”.

## Slide 12: Thank You